## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 9: Synchronous Digital Systems
Instructor: Sagar Karandikar
sagark@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs61c

## Slide 2: You are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today

## Slide 3: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 4: Hardware Design
Next several weeks: how a modern processor is built, starting with basic elements as building blocks
Why study hardware design?
  Understand capabilities and limitations of HW in general and processors in particular
  What processors can do fast and what they can’t do fast (avoid slow things if you want your code to run fast!)
  Background for more in-depth HW courses (CS 150, CS 152)
  Hard to know what you’ll need for next 30 years
  There is only so much you can do with standard processors: you may need to design own custom HW for extra performance
    Even some commercial processors today have customizable hardware!

## Slide 5: Synchronous Digital Systems
Synchronous:
  All operations coordinated by a central clock
    “Heartbeat” of the system!
Digital:
  Represent all values by discrete values
  Two binary digits: 1 and 0
  Electrical signals are treated as 1’s and 0’s
    1 and 0 are complements of each other
  High /low voltage for true / false, 1 / 0
Hardware of a processor, such as the MIPS, is an example of a Synchronous Digital System

## Slide 6: Switches: Basic Element of Physical Implementations
A
Z
Implementing a simple circuit (arrow shows action if wire changes to “1” or is asserted):
Z  A
A
Z
Close switch (if A is “1” or asserted) and turn on light bulb (Z)
Open switch (if A is “0” or unasserted) and turn off light bulb (Z)

## Slide 7: Switches (cont’d)
AND
OR
Z  A and B
Z  A or B
A
B
A
B
Compose switches into more complex ones (Boolean functions):

## Slide 8: Historical Note
Early computer designers built ad hoc circuits from switches
Began to notice common patterns in their work: ANDs, ORs, …
Master’s thesis (by Claude Shannon) made link between work and 19th Century Mathematician George Boole
  Called it “Boolean” in his honor
Could apply math to give theory to hardware design, minimization, …

## Slide 9: Transistors
High voltage (Vdd) represents 1, or true
  In modern microprocessors, Vdd ~ 1.0 Volt
Low voltage (0 Volt or Ground) represents 0, or false
Pick a midpoint voltage to decide if a 0 or a 1
  Voltage greater than midpoint = 1
  Voltage less than midpoint = 0
  This removes noise as signals propagate – a big advantage of digital systems over analog systems
If one switch can control another switch, we can build a computer!
Our switches: CMOS transistors

## Slide 10: CMOS Transistor Networks
Modern digital systems designed in CMOS
  MOS: Metal-Oxide on Semiconductor
  C for complementary: use pairs of normally-open and normally-closed switches
    Used to be called COS-MOS for complementary-symmetry -MOS
CMOS transistors act as voltage-controlled switches
  Similar, though easier to work with, than electro-mechanical relay switches from earlier era
  Use energy primarily when switching
Notes: Wikipedia: The phrase "metal–oxide–semiconductor" is a reference to the physical structure of certain field-effect transistors, having a metal gate electrode placed on top of an oxide insulator, which in turn is on top of a semiconductor material.
CMOS circuits use a combination of p-type and n-type metal–oxide–semiconductor field-effect transistors (MOSFETs)

## Slide 11: CMOS Transistors
n-channel transitor open when voltage at Gate is low closes when:
voltage(Gate) > voltage (Threshold)
(High resistance when gate voltage Low,
Low resistance when gate voltage High)
p-channel transistor closed when voltage at Gate is low opens when:
voltage(Gate) > voltage (Threshold)
(Low resistance when gate voltage Low,
High resistance when gate voltage High)
Three terminals: source, gate, and drain
  Switch action: if voltage on gate terminal is (some amount) higher/lower than source terminal then conducting path established between drain and source terminals (switch is closed)
Gate
Source
Drain
Gate
Source
Drain
Note circle symbol to indicate “NOT” or “complement”
Gate
Drain
Source
Notes: From wikipedia:
The field-effect transistor (FET) relies on an electric field to control the shape and hence the conductivity of a channel of one type of charge carrier in a semiconductor material.
The most commonly used FET is the MOSFET. The CMOS (complementary-symmetry metal oxide semiconductor) process technology is the basis for modern digital integrated circuits. This process technology uses an arrangement where the (usually "enhancement-mode") p-channel MOSFET and n-channel MOSFET are connected in series such that when one is on, the other is off.
CMOS circuits are constructed in such a way that all PMOS transistors must have either an input from the voltage source or from another PMOS transistor. Similarly, all NMOS transistors must have either an input from ground or from another NMOS transistor. The composition of a PMOS transistor creates low resistance between its source and drain contacts when a low gate voltage is applied and high resistance when a high gate voltage is applied.
On the other hand, the composition of an NMOS transistor creates high resistance between source and drain when a low gate voltage is applied and low resistance when a high gate voltage is applied.

## Slide 12: #2: Moore’s Law
Gordon Moore Intel Cofounder B.S. Cal 1950!
# of transistors on an integrated circuit (IC)
Year
Predicts:
2X Transistors / chip every 2 years
Modern microprocessor chips include several billion transistors

## Slide 13: Intel 14nm Technology
Plan view of transistors
Side view of wiring layers

## Slide 14: Scale of the Universe
http://htwins.net/scale2/

## Slide 15: CMOS Circuit Rules
Don’t pass weak values => Use Complementary Pairs
  N-type transistors pass weak 1’s (Vdd - Vth)
  N-type transistors pass strong 0’s (ground)
  Use N-type transistors only to pass 0’s (N for negative)
  Converse for P-type transistors: Pass weak 0s, strong 1s
    Pass weak 0’s (Vth), strong 1’s (Vdd)
    Use P-type transistors only to pass 1’s (P for positive)
  Use pairs of N-type and P-type to get strong values
Never leave a wire undriven
  Make sure there’s always a path to Vdd or GND
Never create a path from Vdd to GND (ground)
  This would short-circuit the power supply!
Notes: Wikipedia: CMOS accomplishes current reduction by complementing every nMOSFET with a pMOSFET and connecting both gates and both drains together. A high voltage on the gates will cause the nMOSFET to conduct and the pMOSFET not to conduct while a low voltage on the gates causes the reverse. This arrangement greatly reduces power consumption and heat generation. However, during the switching time both MOSFETs conduct briefly as the gate voltage goes from one state to another. This induces a brief spike in power consumption and becomes a serious issue at high frequencies.

## Slide 16: CMOS Networks
1V
X
Y
0 Volt
(GND)
x
y
1 Volt
(Vdd)
0V
what is the relationship between x and y?
p-channel transistor closed when voltage at Gate is low opens when:
voltage(Gate) > voltage (Threshold)
n-channel transitor open when voltage at Gate is low closes when:
voltage(Gate) > voltage (Threshold)
Called an inverter or not gate
1 Volt (Vdd)
0 Volt (GND)
Notes: X = 0 implies top switch is closed, so 3V sent Y
X = 0 implies bottom switch is open, so nothing sent to Y
X = 3v implies Top switch is open, so nothing sent to Y
X = 3v implies Bottom switch is closed, so 0V sent Y
Wikipedia:
The image shows what happens when an input is connected to both a PMOS transistor (top of diagram) and an NMOS transistor (bottom of diagram). When the voltage of input X is low, the NMOS transistor's channel is in a high resistance state. This limits the current that can flow from Y to ground.
The PMOS transistor's channel is in a low resistance state and much more current can flow from the supply to the output. Because the resistance between the supply voltage and Y is low, the voltage drop between the supply voltage and Y due to a current drawn from Y is small. The output therefore registers a high voltage.
On the other hand, when the voltage of input X is high, the PMOS transistor is in an OFF (high resistance) state so it would limit the current flowing from the positive supply to the output, while the NMOS transistor is in an ON (low resistance) state, allowing the output to drain to ground.
Because the resistance between Y and ground is low, the voltage drop due to a current drawn into Y placing Y above ground is small. This low drop results in the output registering a low voltage.
In short, the outputs of the PMOS and NMOS transistors are complementary such that when the input is low, the output is high, and when the input is high, the output is low. Because of this behavour of input and output, the CMOS circuits' output is the inverse of the input.

## Slide 17: Two-Input Networks
what is the relationship between x, y and z?
1V
X
Y
0V
Z
x
y
z
0 Volt
1 Volt
0 Volt
1 Volt
0 Volt
0 Volt
1 Volt
1 Volt
1 Volt
1 Volt
1 Volt
0 Volt
Called a NAND gate (NOT AND)
Notes: Top
X = 0v Y = 0V both closed on top, so Z = 3v
X = 0v Y = 0V both open bottom
X = 0v Y = 3V 2nd closed on top, so Z = 3v
X = 0v Y = 3V 2nd in series open
X = 3v Y = 0V 1st closed on top, so Z = 3v
X = 3v Y = 0V 1st in series open
X = 3v Y = 3V both open on top
X = 3v Y = 0V both closed, so Z = 0v

## Slide 18: Clickers/Peer Instruction
x
y
0 Volt
1 Volt
0 Volt
1 Volt
0 Volt
0 Volt
1 Volt
1 Volt
1V
X
Y
0v
Z
Volts
Volts
Volts
Volts
z
0 0 1 1
0 1 0 1
0 1 0 1
1 1 0 0
A B C D
Notes: Top
X = 0v Y = 0V both closed on top, so Z = 3v
X = 0v Y = 0V both open bottom
X = 0v Y = 3V 2nd closed on top, so Z = 3v
X = 0v Y = 3V 2nd in series open
X = 3v Y = 0V 1st closed on top, so Z = 3v
X = 3v Y = 0V 1st in series open
X = 3v Y = 3V both open on top
X = 3v Y = 0V both closed, so Z = 0v

## Slide 19: Administrivia
HW2 out
  We recommend doing this before the midterm
Proj 2-1 out
  Make sure you test your code on hive machines, that’s where we’ll grade them
  Team registration problems? Email Jay

## Slide 20: Administrivia
Midterm this Thursday
  In this room, at this time
  One 8.5”x11” handwritten cheatsheet
  We’ll provide a MIPS green sheet
  No electronics
  Covers up to and including last lecture (07/02)
  TA-led review session tonight (07/06) from 5-8pm in HP Auditorium

## Slide 21: Break

## Slide 22: Combinational Logic Symbols
Common combinational logic systems have standard symbols called logic gates
  Buffer, NOT
  AND, NAND
  OR, NOR
Z
A
B
Z
Z
A
A
B
Inverting versions (NOT, NAND, NOR) easiest to implement with CMOS transistors (the switches we have available and use most)

## Slide 23: Representations of Combinational Logic (groups of logic gates)
Truth Table
Gate Diagram
Boolean Expression
Sum of Products,
Product of Sums Methods
Enumerate Inputs
Enumerate Inputs
Use Equivalency between boolean operators and gates

## Slide 24: Truth Tables for Combinational Logic
F
Y
A
B
C
D
0
Exhaustive list of the output value generated for each combination of inputs

## Slide 25: Truth Table Example #1: y= F(a,b): 1 iff a ≠ b
a | b | y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Y = A B + A B
Y = A + B
XOR

## Slide 26: Truth Table Example #2: 2-bit Adder
How Many Rows?
+
C1
A1
A0
B1
B0
C2
C0

## Slide 27: Truth Table Example #3: 32-bit Unsigned Adder
How Many Rows?

## Slide 28: Truth Table Example #4: 3-input Majority Circuit
Y = A B C + A B C + A B C + A B C
Y = B C + A (B C + B C)
Y = B C + A (B + C)
This is called Sum of Products form;
Just another way to represent the TT as a logical expression
More simplified forms (fewer gates and wires)

## Slide 29: Boolean Algebra
Use plus “+” for OR
  “logical sum”
Use product for AND (ab or implied via ab)
  “logical product”
“Hat” to mean complement (NOT)
Thus
ab + a + c
= ab + a + c
= (a AND b) OR a OR (NOT c )

## Slide 30: Boolean Algebra: Circuit & Algebraic Simplification

## Slide 31: Laws of Boolean Algebra
X X = 0
X 0 = 0
X 1 = X
X X = X
X Y = Y X
(X Y) Z = Z (Y Z)
X (Y + Z) = X Y + X Z
X Y + X = X
X Y + X = X + Y
X Y = X + Y
X + X = 1
X + 1 = 1
X + 0 = X
X + X = X
X + Y = Y + X
(X + Y) + Z = Z + (Y + Z)
X + Y Z = (X + Y) (X + Z)
(X + Y) X = X
(X + Y) X = X Y
X + Y = X Y
Complementarity
Laws of 0’s and 1’s
Identities
Idempotent Laws
Commutativity
Associativity
Distribution
Uniting Theorem
United Theorem v. 2
DeMorgan’s Law

## Slide 32: Boolean Algebraic Simplification Example
Notes: Do on black board
First write truth table
Then minimize and check truth table
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = 1
= a + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 0 1 1

## Slide 33: Boolean Algebraic Simplification Example
a b c y
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 1
Notes: Do on black board
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = 1
= a + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 1

## Slide 34: Clickers/Peer Instruction
Simplify Z = A+BC + A(BC)
A: Z = 0
B: Z = A(1+ BC)
C: Z = (A + BC)
D: Z = BC
E: Z = 1
Notes: Top
X = 0v Y = 0V both closed on top, so Z = 3v
X = 0v Y = 0V both open bottom
X = 0v Y = 3V 2nd closed on top, so Z = 3v
X = 0v Y = 3V 2nd in series open
X = 3v Y = 0V 1st closed on top, so Z = 3v
X = 3v Y = 0V 1st in series open
X = 3v Y = 3V both open on top
X = 3v Y = 0V both closed, so Z = 0v

## Slide 35: In the News: Intel buys Altera
Intel purchased Altera, an FPGA (Field Programmable Gate Array) company for 16.7 billion
Goal is to place reconfigurable hardware on Intel server chips
Take CS150 to learn how to program FPGAs

## Slide 36: Break
(Maybe)

## Slide 37: Signals and Waveforms
an-1
an-1
a0
Noisy!
Delay!

## Slide 38: Signals and Waveforms: Grouping

## Slide 39: Signals and Waveforms: Circuit Delay
2
3
3
4
5
10
0
1
5
13
4
6

## Slide 40: Sample Debugging Waveform

## Slide 41: Type of Circuits
Synchronous Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL) circuits
    Output is a function of the inputs only, not the history of its execution
    E.g., circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    aka “State Elements”
    E.g., memories and registers (Registers)

## Slide 42: Uses for State Elements
Place to store values for later re-use:
  Register files (like $1-$31 in MIPS)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements hold up the movement of information at input to combinational logic blocks to allow for orderly passage

## Slide 43: Accumulator Example
Want: S=0;
for (i=0;i<n;i++)
S = S + Xi
Why do we need to control the flow of information?
Assume:
  Each X value is applied in succession, one per cycle
  After n cycles the sum is present on S
SUM
Xi
S

## Slide 44: First Try: Does this work?
No!
Reason #1: How to control the next iteration of the ‘for’ loop?
Reason #2: How do we say: ‘S=0’?
Feedback

## Slide 45: Second Try: How About This?
Rough timing …
Register is used to hold up the transfer of data to adder
Time
High (1)
Low (0)
High (1)
Low (0)
High (1)
Low (0)
Square wave clock sets when things change
Rounded Rectangle per clock means could be 1 or 0
Xi must be ready before clock edge due to adder delay

## Slide 46: Model for Synchronous Systems
Collection of Combinational Logic blocks separated by registers
Feedback is optional
Clock signal(s) connects only to clock input of registers
Clock (CLK): steady square wave that synchronizes the system
Register: several bits of state that samples on rising edge of CLK (positive edge-triggered) or falling edge (negative edge-triggered)

## Slide 47: Register Internals
n instances of a “Flip-Flop”
Flip-flop name because the output flips and flops between 0 and 1
D is “data input”, Q is “data output”
Also called “D-type Flip-Flop”

## Slide 48: Camera Analogy Timing Terms
Want to take a portrait – timing right before and after taking picture
Set up time – don’t move since about to take picture (open camera shutter)
Hold time – need to hold still after shutter opens until camera shutter closes
Time click to data – time from open shutter until can see image on output (viewscreen)

## Slide 49: Hardware Timing Terms
Setup Time: when the input must be stable before the edge of the CLK
Hold Time: when the input must be stable after the edge of the CLK
“CLK-to-Q” Delay: how long it takes the output to change, measured from the edge of the CLK

## Slide 50: Maximum Clock Frequency
What is the maximum frequency of this circuit?
Max Delay = Setup Time + CLK-to-Q Delay + CL Delay
Hint:
Frequency = 1/Period

## Slide 51: And in Conclusion, …
Multiple Hardware Representations
  Analog voltages quantized to represent logic 0 and logic 1
  Transistor switches form gates: AND, OR, NOT, NAND, NOR
  Truth table mapped to gates for combinational logic design
  Boolean algebra for gate minimization
State Machines
  Finite State Machines: made from Stateless combinational logic and Stateful “Memory” Logic (aka Registers)
  Clocks synchronize D-FF change (Setup and Hold times important!)
  More about these next time